## Slide 1
Diagnostics of electron beams and plasma wave in laser-plasma accelerators
Laszlo Veisz1, Alexander Buck1,2, Maria Nicolai3, Karl Schmid1, Chris M. S. Sears1,
Alexander Sävert3, Julia M. Mikhailova1, Malte C. Kaluza3,4, and Ferenc Krausz1,2
1 Max-Planck-Institut für Quantenoptik, Hans-Kopfermann-Strasse 1, 85748 Garching, Germany
2 Ludwig-Maximilians-Universität München, Am Coulombwall 1, 85748 Garching, Germany
3 Institut für Optik und Quantenelektronik, Friedrich-Schiller-Universität, 07743 Jena, Germany
4 Helmholtz-Institute Jena, Helmholtzweg 4, 07743 Jena, Germany
Notes: 1

## Slide 2
Introduction
Observation of accelerating structure – plasma waves
Temporal characterization of electron bunches
Direct temporal observation of laser wakefield acceleration
Shock-front injection and its temporal characterization
Summary and conclusions
Outline

## Slide 3
Characteristics of
electron bunch and plasma wave
(PIC) simulation
Theory
Experiment
?!?
Accelerated electron beam properties:
Energy spectrum
Charge
Divergence and beam profile
Transverse normalized emittance
Temporal structure and duration (~fs)
…
The accelerating structure −
Important plasma wave properties:
Plasma period / wavelength (~few-10 mm)
Total length (single/ multiple cycles)
Electron bunch position(s)
Amplitude
Accelerating field
electron bunch duration: <10 fs  < 3 mm
plasma wavelength:
~ 5-30 mm
Challenges:
c

## Slide 4
Observation of plasma wave structure
Modena et al., Nature 377, 606 (1995)
D. Umstadter et al., Science 273, 472 (1996)
N. H. Matlis et al., Nature Phys. 2,749 (2006)
P. Dong et al., Phys. Rev. Lett. 104, 134801 (2010)
Frequency-domain
(interferometry)holography
Info about the average
(axially integrated) density
Not really applicable to
short (~lp) laser pulses
Forward Raman scattering
Successful observation of plasma wave
Observation of plasma wave is time integrated
 No time resolution

## Slide 5
Temporal characterization of electron bunches:
Coherent transition radiation
W. P. Leemans et al., Phys. Rev. Lett. 91, 074802 (2003)
Electron
beam
Transition
radiation
Transition radiation (TR): radiation when an electron beam traversing a medium with a (dielectric) discontinuity
Coherent transition radiation (CTR):
- larger amplitude than TR
- its wavelength (THz) depends on
inducing electron beam properties
- observed by laser driven electrons
 Feasible tool to measure bunch duration
Hollow cone
qPeak ~ 1/g
CTR angular distribution
TR CTR
Form factor: info about
bunch distribution
One electron
radiation spectrum

## Slide 6
Temporal characterization:
Coherent transition radiation
(1) J. van Tilborg et al., Phys. Rev. Lett. 96, 014801 (2006)
(2) J. van Tilborg et al., Opt. Lett. 33, 1186 (2008)
(3) G. Berden et al., Phys. Rev. Lett. 93, 114802 (2004)
(3) J. van Tilborg et al., Opt. Lett. 32, 313 (2007)
(3) A. D. Debus et al. Phys. Rev. Lett. 104, 084802 (2010)
Electro optic (EO) sampling (1)
to detect THz field (Pockell´s effect)
Single shot versions:
(Enhanced) spectral encoding* (2)
X-correlation (3)
 30100 fs resolution limited bunch duration
Spectrometer
Short probe
beam
X-correlator (with short probe)
Short probe beam
Detector
*Further development: see talk
from J. van Tilborg Thu 11:20

## Slide 7
Spectrum of
coherent transition radiation
T. Ohkubo et al., PRSTAB 10, 031301(2007)
O. Lundh et al., Nature Phys. 7, 219 (2011)
Careful THz spectral measurements deliver
also the bunch duration!
 Indirect measurement after acceleration
CTR spectrum
Peak of CTR spectrum is at
wCTR te- ≈ 1 or lCTR / (2p) ≈ cte-
wCTR , lCTR : CTR circ. frequency, wavelength
te- : electron bunch duration (RMS)
100-250 fs
Okhubo et al.
1.5 fs (3.5 fs FWHM)
Lundh et al.
See also talk from S. Karsch Mon 15:45

## Slide 8
Observation of
laser plasma acceleration
Potentials of a single-shot, time-resolved technique covering both areas:
  Direct measurement and evolution of electron pulse duration
  Dynamical evolution of plasma wave amplitude (info about beamloading)
  Moment of wave breaking / electron injection

## Slide 9
Polarimetry (Faraday rotation) with 8-fs probe
Shadowgraphy with 8-fs probe
Direct observation of laser-
driven electron acceleration with high spatio-temporal resolution
Plasma wave
Electron bunch
Characterization of the electron bunches
+ direct temporal observation of LWFA
A. Buck et al. Nature Phys., 7, 543 (2011)

## Slide 10
Visualization of the laser wakefield acceleration with
shadowgraphy &
polarimetry
Requirements:
Good spatial and temporal resolution
  Spatial: 2 µm
  Temporal: 8.5 fs  2.6 µm
Experimental setup
A. Buck et al. Nature Phys., 7, 543 (2011)

## Slide 11
Shadowgraphy
Plasma wave
Electron bunch
PIC Simulations
+ Ray-tracing
Explanation:
Requirements to see plasma wave:
Short probe pulse duration
High-resolution and short depth-of-focus
Conclusions:
Same period
Modulation depth ~ plasma wave amplitude
Pos. of max ~ accel. region
A. Buck et al. Nature Phys., 7, 543 (2011)

## Slide 12
Plasma wavelength
Measurement
Theory
Good agreement with theory.
Another proof that modulation in
fact originates from the plasma
wave
No relativistic effects at a=1.67

## Slide 13
Faraday effect for LWFA
Measurement of
Location of the electron bunch
Duration of the electron bunch
(if resolution high enough)
Magnetic field  charge
Rotation of the laser polarization for linearly polarized probe pulse by the magnetic field
  Medium: plasma
Polarization rotation angle:
   Measure jrot and ne to get B-field distribution!
j

## Slide 14
Polarimetry -
Determination of the rotation angle
Camera 2
Camera 1
positive
rot. angle
negative
rot. angle
Advantage of detuned polarizers:
Correct background subs.
Sign of magnetic field
Ratio of intensities visualizes the magnetic field of electron bunch
M. Kaluza et al. Phys. Rev. Lett., 105, 115002 (2011),
A. Buck et al. Nature Phys. 7, 543 (2011)
Detuned

## Slide 15
Faraday Rotation Results
Deconvolution of the electron bunch duration
Averaging over 85 shots:
A. Buck et al. Nature Phys., 7, 543 (2011)
FWHM:
RMS: 2.5 fs

## Slide 16
Combined results #1
Real-time observation of electron bunch and plasma wave (by changing the delay between pump and probe pulse)
„Hidden“ details learned about acceleration:
Electron bunch sits in the first oscillation of the plasma wave
Only one electron bunch visible
Many plasma oscillations are visible
No strong beamloading
Notes: What information can we get when we put both measurements together?

## Slide 17
Laser
Combined results #2
Observed dynamics of LWFA:
Injection point at 200 µm from appearance of Faraday signal
Loading of electrons into the plasma wave and start of acceleration (energy flow) Simultaneous decrease of the number of visible plasma oscillations and the amplitude of the plasma wave
No later injection of electrons only
around 200 µm
from constant rotation angle and bunch duration

## Slide 18
Controlled injection & temporal observation
Diagnostics are applicable
to other experiments even
with high density gradients
Densities & density jump at shockfront could be measured  1.7 : 1
E(MeV)
0 40
0 40
Injection stabilized, acceleration
improved
Energy spread significantly
reduced
Tunable electron energy
Shock-front injection
Self injection
See talk from A. Gonsalves Tue 9:25

## Slide 19
Faraday signal in shock-front injection

## Slide 20
Faraday signal in shock-front injection
Measured duration
Deconvolved duration
Conclusions:
In situ plasma wave / density characterization
Injection after shock front (Electron signal observed ~45 µm later)
FWHM deconvolved duration is 6 fs
No significant other dynamics is observed after the injection in ~100 µm acceleration length
Gas density

## Slide 21: Future directions: single shot movies Frequency-Domain Tomography (FDT)
Compact multi-probe array generation and detection
E = 500 nJ, index evolution due to nonlinear self-focusing of laser pulse
E = 700 nJ, index evolution due to beam collapse and filamentation
By M. C. Downer group, for details: Z. Li, et al., WG5, Wed 4:15 pm, and student poster WG5-45
FDT incorporates index of refraction variation induced phase streaks imprinted on probe profiles at multiple angles and yields a “movie” of evolving index structure in a single shot

## Slide 22: Summary and conclusions
Light Wave Synthesizer 20 with 8 fs pulses is an ideal tool to characterize LWFA
Real-time observation of laser wakefield acceleration (LWFA)
Dynamics of shock-front injection observed
Using few-cycle (sub-10-fs) probe pulses extends the diagnostic capabilities of longer pulse LPA labs
Probe generation in Ti:Sa systems with a (few-)10mJ portion:
  Optical parametric amplification
  Hollow-core fiber
Hollow Core Fibre

## Slide 23
Thank you for your attention !
Acknowledgements:
Munich Center for
Advanced Photonics
Sonderforschungsbereich Transregio 18
Deutsche Forschungsgemeinschaft
Laserlab Europe II

## Slide 24
Properties :
Most intense few-cycle laser system in the world!
optical parametric chirped pulse amplification
130 mJ / pulse
7.7 - 8.5 fs FWHM pulse duration
16 TW power
10 Hz repetition rate
3 µm / 12 µm FWHM focus diameter (F#3 / F#12 optics)
>1019 W/cm2 / 2.5 x 1018 W/cm2 peak intensity
D. Herrmann et al., Opt. Lett. 34, 16 (2009)
The driver laser: Light Wave Synthesizer 20